C-8    LOCATION:  Santa Rosa & Walnut Street   	   CO  SLO	RTE.  01	P.M.  16.77

## DATE  1/06/15                                                                                                                                       Rev2.0

# CONTROL CODE (F)

| INTERVAL | PHASE TIMING |
| --- | --- |
|  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 |  |
| 0 | WALK | 10 | 6 |  | 5 | 10 | 5 | 10 | 5 | 0 |
| 1 | DON’T WK | 10 | 14 |  | 16 | 10 | 11 | 10 | 17 | 1 |
| 2 | MIN GRN | 4 | 7 |  | 4 | 4 | 7 | 4 | 4 | 2 |
| 3 | TYPE 3 | 10 | 10 |  | 10 | 10 | 10 | 10 | 10 | 3 |
| 4 | ADDED | 0.0 | 0.0 |  | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 4 |
| 5 | PASSAGE | 2.0 | 2.0 |  | 2.0 | 2.7 | 2.0 | 1.0 | 2.0 | 5 |
| 6 | MAX GAP | 2.0 | 3.0 |  | 3.0 | 3.7 | 3.0 | 1.0 | 3.0 | 6 |
| 7 | MIN GAP | 1.0 | 1.0 |  | 1.5 | 1.7 | 1.0 | 1.0 | 1.5 | 7 |
| 8 | MAX 1 | 13 | 40 |  | 51 | 13 | 40 | 2 | 61 | 8 |
| 9 | MAX 2 | 50 | 50 |  | 50 | 50 | 50 | 50 | 50 | 9 |
| A | MAX 3 | 50 | 50 |  | 50 | 50 | 50 | 50 | 50 | A |
| B |  |  |  |  |  |  |  |  |  | B |
| C | REDUCE | 0.1 | 0.1 |  | 0.1 | 0.1 | 0.1 | 0.0 | 0.1 | C |
| D | EVERY | 1.0 | 1.0 |  | 1.0 | 1.0 | 1.0 | 1.0 | 1.0 | D |
| E | YELLOW | 3.0 | 3.9 |  | 3.0 | 3.0 | 3.9 | 3.0 | 3.0 | E |
| F | RED CLR | 0.5 | 1.0 |  | 1.0 | 0.5 | 1.0 | 0.0 | 1.0 | F |
| PED XING (ft) |  | 65' |  | 68' |  | 54' |  | 70' |  |
| PRE-EMPTION (E) | FLAGS | (F) |
|  |  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 |  |
| 0 | EV SEL | 0 | PERMIT | 1 | 2 |  | 4 | 5 | 6 |  | 8 | 0 |
| 1 | RR1 CLR | 10 | RED LOCK |  |  |  |  |  |  |  |  | 1 |
| 2 | EVA DLY | 0 | YELLOW LOCK |  |  |  |  |  |  |  |  | 2 |
| 3 | EVA CLR | 30 | VEH RECALL |  | 2 |  |  |  | 6 |  |  | 3 |
| 4 | EVB DLY | 0 | PED RECALL |  |  |  |  |  |  |  |  | 4 |
| 5 | EVB CLR | 20 | PED PHASES |  | 2 |  | 4 |  | 6 |  | 8 | 5 |
| 6 | EVC DLY | 0 | RT OVLA |  |  |  |  |  |  |  |  | 6 |
| 7 | EVC CLR | 30 | RT OVLB |  |  |  |  |  |  |  |  | 7 |
| 8 | EVD DLY | 0 | DBL ENTRY |  |  |  | 4 |  |  |  | 8 | 8 |
| 9 | EVDCLR | 30 | MAX 2 PHASES |  |  |  |  |  |  |  |  | 9 |
| A | MAX EV | 60 | LAG PHASES | FOR OBSERVATION ONLY | A |
| B | RR2 CLR | 10 | RED REST |  |  |  |  |  |  |  |  | B |
| C | EV CLR TMR | * | REST IN WALK |  |  |  |  |  |  |  |  | C |
| D | EV DLY TMR | * | MAX 3 PHASES |  |  |  |  |  |  |  |  | D |
| E | RR CLR TMR | * | YEL START UP |  | 2 |  |  |  | 6 |  |  | E |
| F | RR TIMER | * | FIRST PHASE |  |  |  | 4 |  |  |  |  | F |

ACT MAX 2 GAP  F-C-0 = 3       ACT MAX 2 SET   F-C-1 = 3        CONDITIONAL SERVICE MIN   F-C-2 = 10

MAX VARIABLE INT.    F-0-E = 30          RED REVERT   F-0-F = 2.0          TYPE FLASH    C-0-5 = 1

O/L GRN EXT         (A) F-C-A =               (B) F-C-B =               (C) F-C-C =              (D) F-C-D =

# MAX MODEL 412 PROGRAN MODULE RTCA SWITCH (OFF), LITHIUM BATTERY (NOT) INSTALLED.

# LOCATION: Santa Rosa & Walnut Street

# CONTROL CODE (C)

| LAG FZ | (F) |
| --- | --- |
|  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 |  |
| 0 | FREE |  | 2 |  | 4 |  | 6 |  | 8 | 0 |

# CONTROL CODE (E)

| FUNCTION | (E) |
| --- | --- |
|  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 |  |
| A | O/L (A) NOT |  |  |  |  |  |  |  |  | A |
| B | O/L (B) NOT |  |  |  |  |  |  |  |  | B |
| C | O/L (C) NOT |  |  |  |  |  |  |  |  | C |
| D | O/L (D) NOT |  |  |  |  |  |  |  |  | D |
| FUNCTION | (F) |
|  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 |  |
| 0 | COND CODE 4 |  |  |  |  |  |  |  |  | 0 |
| 1 | COND CODE 5 |  |  |  |  |  |  |  |  | 1 |
| 5 | PHASE 2 PED |  | 2 |  |  |  |  |  |  | 5 |
| 6 | PHASE 6 PED |  |  |  |  |  | 6 |  |  | 6 |
| 7 | PHASE 4 PED |  |  |  | 4 |  |  |  |  | 7 |
| 8 | PHASE 8 PED |  |  |  |  |  |  |  | 8 | 8 |
| A | O/L (A) ON |  |  |  |  |  |  |  |  | A |
| B | O/L (B) ON |  |  |  |  |  |  |  |  | B |
| C | O/L (C) ON |  |  |  |  |  |  |  |  | C |
| D | O/L (D) ON |  |  |  |  |  |  |  |  | D |

# CONTROL CODE (7)

| KEY STROKES 7 + # + HR + MN + CODE + (E) + DOW |
| --- |
| # | HR | MN | ACT CODE | ON/ OFF 0 | DAY OF WEEK |
|  |  |  |  |  | S 1 | M 2 | T 3 | W 4 | T 5 | F 6 | S 7 | # |
| 0 |  |  |  |  |  |  |  |  |  |  |  | 0 |
| 1 |  |  |  |  |  |  |  |  |  |  |  | 1 |
| 2 |  |  |  |  |  |  |  |  |  |  |  | 2 |
| 3 |  |  |  |  |  |  |  |  |  |  |  | 3 |
| 4 |  |  |  |  |  |  |  |  |  |  |  | 4 |
| 5 |  |  |  |  |  |  |  |  |  |  |  | 5 |
| 6 |  |  |  |  |  |  |  |  |  |  |  | 6 |
| 7 |  |  |  |  |  |  |  |  |  |  |  | 7 |
| 8 |  |  |  |  |  |  |  |  |  |  |  | 8 |
| 9 |  |  |  |  |  |  |  |  |  |  |  | 9 |
| A |  |  |  |  |  |  |  |  |  |  |  | A |
| B |  |  |  |  |  |  |  |  |  |  |  | B |
| C |  |  |  |  |  |  |  |  |  |  |  | C |
| D |  |  |  |  |  |  |  |  |  |  |  | D |
| E |  |  |  |  |  |  |  |  |  |  |  | E |
| F |  |  |  |  |  |  |  |  |  |  |  | F |

# LOCATION: Santa Rosa & Walnut Street

## INPUT FILE ASSIGNMEINT

# I FILE

1          2           3          4           5           6           7          8           9         10         11         12         13         14

| U | 1 | 2 | 2 | 2 | 3 | 4 | 4 | 4 | 1 |  | ADV | 2 PED | 6 PED | FLH |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| L |  | 2 | 2 |  |  | 4 | 4 |  | 3 |  | SP1 | 4 PED | 8 PED | STOP TIME |

* SEE NOTES

# ENTER (123) AT ADDRESS F-C-F TO ACCESS DETECTOR PAGE

# CONTROL CODE (E)

| I FILE DETECTORS | PHASE (S) |  | FUNCTION (S) |
| --- | --- | --- | --- |
|  | (C) |  | (D) |
|  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 |  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 |
| 0 | I-1 | 1 |  |  |  |  |  |  |  | 0 |  |  |  |  | 5 | 6 |  |  |
| 1 | I-2-U I-2-L |  | 2 |  |  |  |  |  |  | 1 |  |  |  |  | 5 | 6 |  |  |
| 2 |  |  | 2 |  |  |  |  |  |  | 2 |  |  |  |  | 5 | 6 |  |  |
| 3 | I-3-U I-3-L |  | 2 |  |  |  |  |  |  | 3 |  |  |  |  | 5 | 6 |  |  |
| 4 |  |  | 2 |  |  |  |  |  |  | 4 |  |  |  |  | 5 | 6 |  |  |
| 5 | I-4 |  | 2 |  |  |  |  |  |  | 5 |  |  |  |  | 5 | 6 |  |  |
| 6 | I-5 |  |  | 3 |  |  |  |  |  | 6 |  |  |  |  | 5 | 6 |  |  |
| 7 | I-6-U I-6-L |  |  |  | 4 |  |  |  |  | 7 |  |  |  |  | 5 | 6 |  |  |
| 8 |  |  |  |  | 4 |  |  |  |  | 8 |  |  |  |  | 5 | 6 |  |  |
| 9 | I-7-U I-7-L |  |  |  | 4 |  |  |  |  | 9 |  |  |  |  | 5 | 6 |  |  |
| A |  |  |  |  | 4 |  |  |  |  | A |  |  |  |  | 5 | 6 |  |  |
| B | I-8 |  |  |  | 4 |  |  |  |  | B |  |  |  |  | 5 | 6 |  |  |
| C | I-9-U I-9-L | 1 |  |  |  |  |  |  |  | C |  |  |  |  | 5 | 6 |  |  |
| D |  |  |  | 3 |  |  |  |  |  | D |  |  |  |  | 5 | 6 |  |  |

# DETECTOR FUNCTIONS

1 – RED LOCK          2 – YELLOW LOCK          5 – EXTENSION

6 – COUNT          7 – CALL          8 – TYPE 3 DISCONNECT

LOCATION:	 Santa Rosa & Walnut Street

## INPUT FILE ASSIGNMENT

## J FILE

1           2           3          4           5           6           7          8           9         10         11         12         13         14

| U | 5 | 6 | 6 | 6 | 7 | 8 | 8 | 8 | 5 |  | SP2 | EVA 2&5 | EVB 4&7 | RR1 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| L |  | 6 | 6 |  |  | 8 | 8 |  | 7 |  | SP3 | EVC 1&6 | EVD 3&8 | RR2 |

* SEE NOTES

# ENTER (123) AT ADDRESS F-C-F TO ACCESS DETECTOR PAGE

# CONTROL CODE (E)

| J FILE DETECTORS | PHASE (S) |  | FUNCTION (S) |
| --- | --- | --- | --- |
|  | (E) |  | (F) |
|  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 |  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 |
| 0 | J-1 |  |  |  |  | 5 |  |  |  | 0 |  |  |  |  | 5 | 6 |  |  |
| 1 | J-2-U J-2-L |  |  |  |  |  | 6 |  |  | 1 |  |  |  |  | 5 | 6 |  |  |
| 2 |  |  |  |  |  |  | 6 |  |  | 2 |  |  |  |  | 5 | 6 |  |  |
| 3 | J-3-U J-3-L |  |  |  |  |  | 6 |  |  | 3 |  |  |  |  | 5 | 6 |  |  |
| 4 |  |  |  |  |  |  | 6 |  |  | 4 |  |  |  |  | 5 | 6 |  |  |
| 5 | J-4 |  |  |  |  |  | 6 |  |  | 5 |  |  |  |  | 5 | 6 |  |  |
| 6 | J-5 |  |  |  |  |  |  | 7 |  | 6 |  |  |  |  | 5 | 6 |  |  |
| 7 | J-6-U J-6-L |  |  |  |  |  |  |  | 8 | 7 |  |  |  |  | 5 | 6 |  |  |
| 8 |  |  |  |  |  |  |  |  | 8 | 8 |  |  |  |  | 5 | 6 |  |  |
| 9 | J-7-U J-7-L |  |  |  |  |  |  |  | 8 | 9 |  |  |  |  | 5 | 6 |  |  |
| A |  |  |  |  |  |  |  |  | 8 | A |  |  |  |  | 5 | 6 |  |  |
| B | J-8 |  |  |  |  |  |  |  | 8 | B |  |  |  |  | 5 | 6 |  |  |
| C | J-9-U J-9-L |  |  |  |  | 5 |  |  |  | C |  |  |  |  | 5 | 6 |  |  |
| D |  |  |  |  |  |  |  | 7 |  | D |  |  |  |  | 5 | 6 |  |  |

# DETECTOR FUNCTIONS

1 – RED LOCK          2 – YELLOW LOCK          5 – EXTENSION

6 – COUNT          7 – CALL          8 – TYPE 3 DISCONNECT

# LOCATION: Santa Rosa & Walnut Street

# CONTROL CODE (D)

| DET. | DELAY | CARYOVER |  | DET. | DELAY | CARRYOVER |
| --- | --- | --- | --- | --- | --- | --- |
| I1 | D-1-0 | . | D-3-0 | . |  | J1 | D-2-0 | . | D-4-0 | . |
|  | D-7-0 | * | D-9-0 | * |  |  | D-8-0 | * | D-A-0 | * |
| I2U | D-1-1 | . | D-3-1 | 1.5 |  | J2U | D-2-1 | . | D-4-1 | 1.5 |
|  | D-7-1 | * | D-9-1 | * |  |  | D-8-1 | * | D-A-1 | * |
| I2L | D-1-2 | . | D-3-2 | 1.5 |  | J2L | D-2-2 | . | D-4-2 | 1.5 |
|  | D-7-2 | * | D-9-2 | * |  |  | D-8-2 | * | D-A-2 | * |
| I3U | D-1-3 | . | D-3-3 | . |  | J3U | D-2-3 | . | D-4-3 | . |
|  | D-7-3 | * | D-9-3 | * |  |  | D-8-3 | * | D-A-3 | * |
| I3L | D-1-4 | . | D-3-4 | . |  | J3L | D-2-4 | . | D-4-4 | . |
|  | D-7-4 | * | D-9-4 | * |  |  | D-8-4 | * | D-A-4 | * |
| I4 | D-1-5 | . | D-3-5 | . |  | J4 | D-2-5 | . | D-4-5 | . |
|  | D-7-5 | * | D-9-5 | * |  |  | D-8-5 | * | D-A-5 | * |
| I5 | D-1-6 | . | D-3-6 | . |  | J5 | D-2-6 | . | D-4-6 | . |
|  | D-7-6 | * | D-9-6 | * |  |  | D-8-6 | * | D-A-6 | * |
| I6U | D-1-7 | . | D-3-7 | . |  | J6U | D-2-7 | . | D-4-7 | 0.5 |
|  | D-7-7 | * | D-9-7 | * |  |  | D-8-7 | * | D-A-7 | * |
| I6L | D-1-8 | 15.0 | D-3-8 | . |  | J6L | D-2-8 | 10.0 | D-4-8 | 1.0 |
|  | D-7-8 | * | D-9-8 | * |  |  | D-8-8 | * | D-A-8 | * |
| I7U | D-1-9 | . | D-3-9 | . |  | J7U | D-2-9 | . | D-4-9 | . |
|  | D-7-9 | * | D-9-9 | * |  |  | D-9-9 | * | D-A-9 | * |
| I7L | D-1-A | . | D-3-A | . |  | J7L | D-2-A | . | D-4-A | . |
|  | D-7-A | * | D-9-A | * |  |  | D-8-A | * | D-A-A | * |
| I8 | D-1-B | . | D-3-B | . |  | J8 | D-2-B | . | D-4-B | . |
|  | D-7-B | * | D-9-B | * |  |  | D-8-B | * | D-A-B | * |
| I9U | D-1-C | . | D-3-C | . |  | J9U | D-2-C | . | D-4-C | . |
|  | D-7-C | * | D-9-C | * |  |  | D-8-C | * | D-A-C | * |
| I9L | D-1-D | . | D-3-D | . |  | J9L | D-2-D | . | D-4-D | . |
|  | D-7-D | * | D-9-D | * |  |  | D-8-D | * | D-A-D | * |

* OBSERVE TIMERS

*SET F-C-F = 112,  E-6-F = 1,  F-C-F = 0  (Transition Reduction Method OFF)*

### NUMBER OF POWER FAILURES      F-0-C = LONG      F-0-D = SHORT

### LAST POWER FAILURE     D-A-E = HOUR    D-B-E = MINUTE    D-C-E = DAY

### LAST FLASH    D-A-F = HOUR    D-B-F = MINUTE    D-C-F = DAY

### LITHIUM BATTERY CONDITION OBSERVED AT D-E-F       84 = BAD      85 = GOOD

### D-E-E = C-8 VERSION #  004               F-C-3 = TYPE  MAX

D-E-C = 007,  D-E-D = 107

# LOCATION: Santa Rosa & Walnut Street

# MASTER LOCATION:  Santa Rosa & Highland Drive

# CONTROL CODE (C)

| INTERVAL | CONTROL PLANS |
| --- | --- |
|  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 |  |  |
| 0 | CYCLE | 120 | 120 | 132 |  |  |  |  | 110 |  | 0 |
| 1 | FZ 1 GF | 14 | 11 | 10 |  |  |  |  | 16 |  | 1 |
| 2 | COORD FZ | ---- | ---- | ---- | ---- | ---- | ---- | ---- | ---- | ---- | 2 |
| 3 | FZ 3 GF |  |  |  |  |  |  |  |  |  | 3 |
| 4 | FZ 4 GF | 35 | 55 | 23 |  |  |  |  | 48 |  | 4 |
| 5 | FZ 5 GF | 12 | 10 | 8 |  |  |  |  | 16 |  | 5 |
| 6 | COORD FZ | ---- | ---- | ---- | ---- | ---- | ---- | ---- | ---- | ---- | 6 |
| 7 | FZ 7 GF |  |  |  |  |  |  |  |  |  | 7 |
| 8 | FZ 8 GF | 50 | 55 | 23 |  |  |  |  | 48 |  | 8 |
| 9 | X CYCLE |  |  | 0.5 |  |  |  |  |  |  | 9 |
| A | OFFSET A | 57 | 71 | 48 |  |  |  |  | 61 |  | A |
| B | OFFSET B |  |  |  |  |  |  |  |  |  | B |
| C | OFFSETC |  |  |  |  |  |  |  |  |  | C |
| D | FZ 3 EXT |  |  |  |  |  |  |  |  |  | D |
| E | FZ 7 EXT |  |  |  |  |  |  |  |  |  | E |
| F | INTERRUPT |  |  |  |  |  |  |  |  |  | F |

| LAG FZ GAPOUT (E) | LAG FZ | (F) |
| --- | --- | --- |
|  |  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 |  |
| 1 | PLAN 1 |  | PLAN 1 |  | 2 |  | 4 |  | 6 |  | 8 | 1 |
| 2 | PLAN 2 | 1 | PLAN 2 |  | 2 |  | 4 | 5 |  |  | 8 | 2 |
| 3 | PLAN 3 | 1 | PLAN 3 |  | 2 |  | 4 | 5 |  |  | 8 | 3 |
| 4 | PLAN 4 |  | PLAN 4 |  | 2 |  | 4 |  | 6 |  | 8 | 4 |
| 5 | PLAN 5 |  | PLAN 5 |  | 2 |  | 4 |  | 6 |  | 8 | 5 |
| 6 | PLAN 6 |  | PLAN 6 |  | 2 |  | 4 |  | 6 |  | 8 | 6 |
| 7 | PLAN 7 |  | PLAN 7 |  | 2 |  | 4 |  | 6 |  | 8 | 7 |
| 8 | PLAN 8 |  | PLAN 8 |  | 2 |  | 4 |  | 6 |  | 8 | 8 |
| 9 | PLAN 9 |  | PLAN 9 |  | 2 |  | 4 |  | 6 |  | 8 | 9 |
| C |  |  | COORD FZ |  | 2 |  |  |  | 6 |  |  | C |

| TIME BASE SELECT F-D-0 = 1 TIME BASE HOUR F-D-1 = 0 TIME BASE MINUTE F-D-2 = 0 PED SELECT F-D-3 = 0 7-WIRE SELECT F-D-4 = 0 PERMISSIVE SELECT F-D-5 = 0 OFFSET SEEK F-D-8 = 1 LIMITED DOWNLOAD C-C-2 = 0 | # OF SLAVES D-0-0 = 00 MANUAL PLAN C-0-1 * MASTER PLAN C-0-2 * CURRENT PLAN C-0-3 * LAST PLAN C-0-4 * CURRENT OFFSET C-0-6 TRANSMIT PLAN C-0-7 MANUAL OFFSET C-0-D |
| --- | --- |

* FOR OBSERVATION ONLY

# LOCATION: Santa Rosa & Walnut Street

# CONTROL CODE (9)

| KEY STROKES 9 + # + HR + MN + PLAN + OS + (E) + DOW |
| --- |
| # | HR | MN | PLAN | OFF SET | DAY OF WEEK | # |
|  |  |  |  |  | S 1 | M 2 | T 3 | W 4 | T 5 | F 6 | S 7 |  |
| 0 | 07 | 20 | 1 | A |  | 2 | 3 | 4 | 5 | 6 |  | 0 |
| 1 | 09 | 30 | 8 | A |  | 2 | 3 | 4 | 5 | 6 |  | 1 |
| 2 | 11 | 00 | 2 | A |  | 2 | 3 | 4 | 5 | 6 |  | 2 |
| 3 | 18 | 30 | 8 | A |  | 2 | 3 | 4 | 5 | 6 |  | 3 |
| 4 | 19 | 30 | E |  |  | 2 | 3 | 4 | 5 | 6 |  | 4 |
| 5 | 11 | 30 | 8 | A | 1 |  |  |  |  |  | 7 | 5 |
| 6 | 17 | 00 | E |  | 1 |  |  |  |  |  |  | 6 |
| 7 | 18 | 00 | E |  |  |  |  |  |  |  | 7 | 7 |
| 8 | 15 | 30 | 3 | A |  | 2 | 3 | 4 | 5 | 6 |  | 8 |
| 9 | 17 | 45 | 2 | A |  | 2 | 3 | 4 | 5 | 6 |  | 9 |
| A |  |  |  |  |  |  |  |  |  |  |  | A |
| B |  |  |  |  |  |  |  |  |  |  |  | B |
| C |  |  |  |  |  |  |  |  |  |  |  | C |
| D |  |  |  |  |  |  |  |  |  |  |  | D |
| E |  |  |  |  |  |  |  |  |  |  |  | E |
| F |  |  |  |  |  |  |  |  |  |  |  | F |

| LOCATION DIP SWITCH |  |  | FEATURE DIP SWITCH |
| --- | --- | --- | --- |
|  | OFF | ON |  |  |  | OFF | ON |
| 1 |  | ON |  |  | 1 | X |  |
| 2 | X |  |  |  | 2 | X |  |
| 3 |  | ON |  |  | 3 | X |  |
| 4 | X |  |  |  | 4 | X |  |
| 5 | X |  |  |  | 5 | X |  |
| 6 | X |  |  |  | 6 | X |  |
| 7 | X |  |  | 7 | X |  |
| 8 | X |  |  | 8 | X |  |

## CLOCK RESET F-9-0 = 0

### FOR OBSERVATION ONLY

LOCATION C-0-0 = 005 LOCAL CYCLE TIMER C-A-0 MASTER CYCLE TIMER C-B-0 PRESENT OFFSET C-A-A DESIRED OFFSET C-B-A HOLD C-F-D PHASE NEXT C-F-E FORCE OFF PHASE C-F-F CALCULATED FORCE OFF C-A-1 to C-A-8 PERMISSIVE PERIOD C-B-1 to C-B-8

# LOCATION: Santa Rosa & Walnut Street

# CONTROL CODE (D)

| MAX RECALL | (D) |
| --- | --- |
|  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 |  |
| 1 | PLAN 1 |  |  |  |  |  |  |  |  | 1 |
| 2 | PLAN 2 |  |  |  |  |  |  |  |  | 2 |
| 3 | PLAN 3 |  |  |  |  |  |  |  |  | 3 |
| 4 | PLAN 4 |  |  |  |  |  |  |  |  | 4 |
| 5 | PLAN 5 |  |  |  |  |  |  |  |  | 5 |
| 6 | PLAN 6 |  |  |  |  |  |  |  |  | 6 |
| 7 | PLAN 7 |  |  |  |  |  |  |  |  | 7 |
| 8 | PLAN 8 |  |  |  |  |  |  |  |  | 8 |
| 9 | PLAN 9 |  |  |  |  |  |  |  |  | 9 |

| MIN RECALL | (E) |
| --- | --- |
|  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 |  |
| 1 | PLAN 1 |  |  |  |  |  |  |  |  | 1 |
| 2 | PLAN 2 |  |  |  |  |  |  |  |  | 2 |
| 3 | PLAN 3 |  |  |  |  |  |  |  |  | 3 |
| 4 | PLAN 4 |  |  |  |  |  |  |  |  | 4 |
| 5 | PLAN 5 |  |  |  |  |  |  |  |  | 5 |
| 6 | PLAN 6 |  |  |  |  |  |  |  |  | 6 |
| 7 | PLAN 7 |  |  |  |  |  |  |  |  | 7 |
| 8 | PLAN 8 |  |  |  |  |  |  |  |  | 8 |
| 9 | PLAN 9 |  |  |  |  |  |  |  |  | 9 |

| PED RECALL | (F) |
| --- | --- |
|  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 |  |
| 1 | PLAN 1 |  |  |  |  |  |  |  |  | 1 |
| 2 | PLAN 2 |  |  |  |  |  |  |  |  | 2 |
| 3 | PLAN 3 |  |  |  |  |  |  |  |  | 3 |
| 4 | PLAN 4 |  |  |  |  |  |  |  |  | 4 |
| 5 | PLAN 5 |  |  |  |  |  |  |  |  | 5 |
| 6 | PLAN 6 |  |  |  |  |  |  |  |  | 6 |
| 7 | PLAN 7 |  |  |  |  |  |  |  |  | 7 |
| 8 | PLAN 8 |  |  |  |  |  |  |  |  | 8 |
| 9 | PLAN 9 |  |  |  |  |  |  |  |  | 9 |
| A | TOD MAX RECALL 1 |  |  |  |  |  |  |  |  | A |
| B | TOD MAX RECALL 2 |  |  |  |  |  |  |  |  | B |

# LOCATION: Santa Rosa & Walnut Street

# MASTER LOCATION:  _________________________

# CONTROL CODE (C)

| LAG FZ | (F) |
| --- | --- |
|  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 |  |
| A | Y-COORD (C ) |  |  |  |  |  |  |  |  | A |
| B | Y-COORD (D) |  |  |  |  |  |  |  |  | B |

# CONTROL CODE (E)

| LAG FZ | (F) |
| --- | --- |
|  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 |  |
| 2 | Y-COORD RECALL |  |  |  |  |  |  |  |  | 2 |
| 3 | Y-COORD RECALL |  |  |  |  |  |  |  |  | 3 |

# CONTROL CODE (C)

| INTERVAL | Y-COORD |
| --- | --- |
|  | C | D |  |
| 4 | PERM TIME |  |  | 4 |
| 5 | LAG OFFSET |  |  | 5 |
| 6 | FORCE OFF |  |  | 6 |
| 7 | LONG GREEN |  |  | 7 |
| 8 | NO GREEN |  |  | 8 |
| A | COORD OFFSET |  |  | A |

## Y-COORD TIMERS

## FOR OBSERVATION ONLY

CONTROL CODE  (C) + (C or D)

| 9 | PERM. |
| --- | --- |
| B | OFFSET |
| C | LAG GREEN |
| D | FORCE OFF |
| E | LONG GREEN |
| F | NO GREEN |

# Text boxes

##### ACTIVITY CODES

1     MAX TERMINATION

- MAX 2

- MAX 3

- COND SERV CODE 4

- COND SERV CODE 5

- AUX OUTPUT 6

- AUX OUTPUT 7

- AUX OUTPUT 8

- MAX RECALL 1

A    ACT MAX 2

B     MAX RECALL 2

C     YELLOW COORD C

D     YELLOW COORD D

E      FREE OPERATION

F      FLASH OPERATION

##### INTERVALS

- WALK

- PED CLEARANCE

- MINIMUM

4    VARIABLE INITIAL

- PASSAGE

- REDUCED GAP

- RED REST

- PREEMPT

A    STOP TIME

B    RED REVERT

C   GAP TERM YELLOW

D   MAX TERM YELLOW

E    FORCEOFF YELLOW

F    RED CLEARANCE